Managing Safe Work Practices – General Work Permit

Americas Products – Standardized OE Process

Version 1.0
Approved: 14 March 2011

© 2011 by Chevron Products Company (a Chevron U.S.A. Inc. division)

This document contains proprietary information of Chevron Corporation. Any use of this document without express, prior, written permission from Chevron Corporation and/or its affiliates is prohibited.

Managing Safe Work Practices – General Work Permit Standard

Contents

1	Purpose, Objectives and Scope	3

2	Terms and Definitions	4

3	Roles, Responsibilities and Training Requirements	7

4	Standard Instructions	8

5	Records	14

6	References	16

7	Other Guidance Documents	16

8	Revision History	17

Appendix A: General Work Permit Example	18

# Purpose, Objectives and Scope

## Purpose

The purpose of this standard is to ensure that all permitted work is performed in a safe and controlled manner.

## Objective

This standard establishes minimum requirements for issuing General Work Permits at Chevron Downstream & Chemicals facilities or job sites.

Note: Each Downstream & Chemicals strategic business unit (SBU) or business unit (BU) or location may have additional regulatory requirements.

## Scope

This standard applies to all Chevron employees and contractors working at Chevron Downstream & Chemicals facilities, job sites and/or any joint venture operations where joint venture agreements allow its use.

This standard does not apply to routine tasks performed at Chevron Downstream & Chemicals facilities.

# Terms and Definitions

The following terms and definitions apply to the Americas Products – Safe Work Practices (SWP) General Work Permit Standard:

| Term | Definitions |
| --- | --- |
| Approved Written Work Procedure | A written procedure developed by competent personnel using risk management considerations that have been approved, as appropriate, and maintained in a retrievable filing system in electronic or hard-copy format. The procedure lists task-oriented steps that have a starting and ending point and details how work is to be completed using the SWPs and guidelines or other materials (where appropriate). The procedure also identifies the activities, roles, responsibilities and authorities assigned to all the parties involved. |
| Classified Hazardous Area | Any area classified as a hazardous zone area (Zone 0, 1 or 2 or Class I, Division 1 or 2) in accordance with the American Petroleum Institute Recommended Practice (API RP) 505/API RP 500 or other equivalent local standards. |
| Company Representative | A Chevron employee who is responsible for liaising with and managing the contractor to ensure that the contractor performs the work safely in accordance with applicable SWP standards. |
| Competent Person | An individual who has the skills, knowledge, experience, judgment and ability to perform the specific assigned tasks or activities to meet requirements of the relevant SWPs. Note: The competent person may vary for each SWP or element of those SWPs. |
| Confined Space | This definition may differ by SBU/BU depending on the local regulatory requirements. Generally, confined space means any space that meets all of the following criteria: A person can bodily enter the space and perform assigned work; The space has limited means of entry and exit; The space is not designed for continuous occupancy; and The space contains (has contained or has the potential to contain) a hazardous atmosphere. |
| Confined Space Entry | The act of passing any major portion of the body (such as head, torso or legs) through an opening to a confined space. Entry is considered to have occurred as soon as the body part breaks the plane of the opening. Note: A Qualified Gas Tester may insert a portion of the hand and arm in the space for gas detection purposes. |
| Confined Space Entry Form | A form used by the Permit Issuer to grant approved personnel permission to perform safe entry into a confined space. Note: Entry into a confined space requires both a valid General Work Permit and a Confined Space Entry Form. A Confined Space Entry Form allows entry only into a confined space; no work is allowed to be performed under the Confined Space Entry Form itself. For work to be performed within any confined space the work must be covered under the relevant General Work Permit and/or Hot Work Form. |
| General Work | All non-routine work or periodic work for which approved written operating procedures do not exist and which does not involve a source of ignition and/or entry into a confined space. General work might also be referred to as cold work or safe work. Note: Emergency response work carried out during the initial containment (control) phase of an emergency is excluded from the definition of general work for the purposes of this standard and as such does not specifically require the use of a Work Permit, but must still be carried out in a controlled and managed fashion. Ongoing response work after the containment phase, i.e. clean-up work, does fall within this definition of general work. |
| General Work Permit | The written or printed document or collection of documents that is provided by the Permit Issuer to allow and control work. |
| Hazardous Area | Any classified hazardous area and/or those areas of a facility where flammable liquids, gases or vapors are present on a continual, intermittent or periodic basis and/or where flammable liquids, gases or vapors may be present but are confined within closed containers or systems under normal operating conditions. |
| Hazardous Atmosphere | Atmosphere(s) that expose personnel to the risk of death, incapacitation, impaired ability to self-rescue, injury, or acute or chronic illness that may be caused by any of the following: An atmospheric concentration of any substance that could result in personnel exposure in excess of the permissible exposure limit (PEL), such as benzene or hydrogen sulfide. Flammable gas, vapor or mist in excess of 10 percent of its lower flammable limit (LFL). An atmospheric oxygen concentration less than 19.5 percent or more than 23 percent. Any other atmospheric condition that is immediately dangerous to life or health (IDLH). |
| High-Risk Work | Job tasks involving the following SWPs: Confined space entry Electrical work Hot work Isolation of hazardous energy Work at heights Additional SWRs identified by the SBU/BU Excavation |
| Hot Work | Any operation or job that could provide, become or create an ignition source for any flammable or combustible material in a hazardous area. |
| Hot Work Form | A form issued in addition to a General Work Permit to grant approved personnel permission to perform hot work. |
| Job Safety Analysis (JSA) | A detailed, written hazard assessment that breaks down a job task into the sequence of steps required to do the following: perform the task identify the hazards specific to each step evaluate hazard risk detail mitigation measures to eliminate or manage the risk Note: The job task is broken down into the sequence of steps required to perform the task, the potential hazards/risk for each of these steps are determined, and the controls necessary to eliminate or mitigate those hazards/risks are developed. |
| Lower Flammable Limit (LFL) | The lowest mixture of hydrocarbon vapor and air that will support combustion. LFL is typically indicated on gas testing equipment as 100 percent and is sometimes referred to as lower explosive limit (LEL). |
| Non-Routine Task | Any operational or maintenance activity performed within an operating area that is outside of the operator or maintenance worker's normal work duties where no approved written work procedure exists, for example, any task involving hot work or line-breaking by operational, maintenance, or contractor personnel. |
| Permissible Exposure Limit (PEL) | An exposure limit to a chemical as established by Chevron Corporation and/or a local regulatory authority. May be either a: Time-weighted average limit (TWA or short-term exposure limit [STEL]) Maximum concentration exposure limit (such as a ceiling limit) |
| Permit Approver | A competent individual who has been trained, tested and authorized by the Company to review and, where applicable, sign and approve the relevant forms. Business Unit Local Management will determine if a Permit Approver will be required to review and approve permitted job tasks deemed as ‘high risk’ permitted work. |
| Permit Extension | Prolonging the time period (within the same work shift) for which the permit was originally written. |
| Permit Issuer | A competent and trained individual who has been authorized by the Company to complete, review and issue the various types of work permits and work forms for their assigned area. Business units can determine if the Permit Issuer may also serve as the Permit Approver or whether an additional level of approval is required. |
| Permit Renewal | Reissuing of an existing work permit for a subsequent shift. |
| Permit Requester or Permit Holder | A competent individual who knows the requirements of general work permits; who reviews, signs and accepts an issued work permit; and who is responsible for ensuring that all requirements and conditions of the issued work permit and all related permit documentation are met. As a minimum the Permit Requester must have undertaken Awareness training (or equivalent) on the AP SWPs. |
| Person in Charge | A competent individual who is responsible for an assigned area and the safe execution of work in that area. The designated person may vary, depending on the work specified. Note: Sometimes call Responsible Person/Party. |
| Qualified Gas Tester | A person who is trained and has been tested in the use of portable gas testing equipment and has successfully demonstrated use of the equipment in the field. This person must also be trained to recognize hazards inherent in hot work and confined space entry. |
| Routine Task | Any task performed where the operations or maintenance personnel are trained in the task and familiar with all of the hazards associated with the task, and there is an approved written procedure for the tasks. Generally the task is performed at least once a month. There is a very low probability of change of work scope or conditions that would generate previously unidentified or unanticipated hazards. |
| Self-Permitting | A permitting process where a pre-approved contractor self-permits and supervises work to be performed at locations where no Chevron Permit Issuer is present. |
| Work Form | A document used to identify the controls required to perform specific tasks such as high-voltage electrical isolation, excavation, hot work and confined space entry. |
| Work Plan | A document describing in detail the activities, tasks and sub-tasks required to complete a specific scope of work. Note: The scale and detail of the Work Plan will vary based upon the complexity of the work. For short duration, non-complex activities the work plan may constitute the work order, relevant LPS tools (e.g. JLA), and the relevant Work Permit(s) and Form(s). For longer duration ‘project type’ work or more complex activities a separate Work Plan document may apply. Work plans are mandatory for all High Risk work and recommended for all other work. |

# Roles, Responsibilities and Training Requirements

There must be clearly defined roles, and personnel must meet the training and competency requirements of this standard prior to starting work. SBU/BU or country regulations may specify additional training and competency requirements.

A single individual may fulfill more than one role as long as he or she meets all of the competency requirements and is able to fully meet multiple responsibilities. For example, a Permit Issuer may also serve as a Gas Tester. When selecting personnel for these positions, consideration should be given to their level of experience and their past performance.

The following roles and responsibilities are specific to general work permitting and are further defined in the Downstream & Chemicals – SWP Training Requirements Tool:

Permit Approver

Permit Issuer

Permit Requester or Permit Holder

There may be additional SWPs and roles needed for performing the permitted work, such as gas detection, confined space entry, hot work or isolation of hazardous energy. Refer to the Roles, Responsibilities and Training Requirements section of the applicable SWP standard (see 6.0 – References section and 7.0 – Other Guidance Documents section of this document) for additional relevant roles.

## Initial Training

Personnel must meet the competency requirements prior to starting work. Refer to the Downstream & Chemicals – SWP Training Requirements Tool.

## Refresher Training

Refresher training must be provided as follows:

Whenever an individual demonstrates insufficient knowledge of the Downstream & Chemicals – SWP General Work Permit Standard

At least every three years

Whenever an incident has occurred where the root cause indicates a lack of knowledge of the work permit process

# Standard Instructions

The General Work Permit system serves a dual purpose: it is both an administrative control to ensure work is authorized prior to its execution and a means for identifying and communicating the precautions and restrictions necessary to perform the work safely.

Work involving the SWPs listed below is deemed high risk work and must be authorized prior to the start of work. Depending on the hazard assessment, the Americas Products – SWP Gas Detection Standard may be applicable. Refer to the relevant Downstream & Chemicals SWP for more information.

Confined space entry

Electrical work

Hot work

Isolation of hazardous energy

Work at heights

Excavation

## Assessing and Managing Hazards

All high risk work must be permitted and managed in accordance with the Americas Products – Managing SWPs Assessing Hazards and Managing High-Risk Work Procedure.

For all other work that requires a work permit to be issued, SBUs/BUs may:

Specify the degree of rigor required to identify the potential hazards associated with the requested work

Determine the controls necessary to ensure the work can be performed safely

In addition, the Americas Products – Managing SWPs Assessing Hazards and Managing High-Risk Work Procedure. requires that appropriate personnel:

Conduct a hazard assessment using appropriate subject matter experts.

Physically inspect/walk the job site prior to signing the permit.

Write a JLA or an approved, written work procedure.

Create a written work plan.

Conduct a pre-job briefing with personnel – or when changes in personnel occur – before performing work.

Ensure that a field review of work in progress occurs at least once during a work shift (or once during a 24-hour time period).

All individuals have the authority and responsibility to stop the work if an unsafe condition occurs or if there is uncertainty about the scope of work or work plan.

Note 1: A pre-job safety briefing is required to be held each day work is undertaken and a new Safety Briefing form completed, even if the work is a continuation of the previous day’s work using a work permit which has been renewed.

Note 2: The Permit Issuer or his delegated alternate shall record field reviews on the pre-job safety briefing form by recording the time of the review and initialing the form.

## Documentation

### General Work Permit

General Work Permits are typically distinguishable from the other types of work forms through the use of a color-coding scheme with a unique sequential number. The permits shall be available in duplicate as a minimum. In those countries where English is not the primary language, the permit shall be provided in the predominate language of the country and/or the people conducting the work. See Appendix A: General Work Permit for an example.

The General Work Permit is broken into three sections: A, B and C. The request for and completion of the General Work Permit requires:

Section A – to be completed by the Permit Requester or Permit Holder and submitted to the Permit Issuer as a request for work

Section B – to be completed by the Permit Issuer

Section C – to be signed by the designated parties as applicable

The General Work Permit must list the following information:

Time span that the work permit is valid

Name of the Permit Requester

Company requesting the permit

Company facility name

Description of the work to be done with job limitations noted

Location of the job site or area

What the equipment last contained (if applicable)

Gas test results, if required (for example, LFL/LEL, O2 and H2S)

Any specialty testing required and the results

Hazardous energy isolation requirements (see the Americas Products – SWP Isolation of Hazardous Energy Standard)

Specific hazards identified in the pre-job risk assessment

Cross-reference to other permit forms and applicable documentation

Number of workers at job site (to include the Permit Requester or Permit Holder)

Identification of special tools/equipment required to do the work safely

The precautions and restrictions (control measures) required to eliminate or mitigate identified or anticipated hazards

Space for the signature of the Permit Requester or Permit Holder and the date the form was signed

Space for the signature of the Permit Issuer and the date the form was signed

Space for the signature of the Permit Approver (when applicable) and the date the form was signed

Space for the supervisor’s, or designate’s, signature to verify review of work in progress (optional)

Space for the signatures of affected personnel to acknowledge they were included in the pre-job briefing (optional)

Space to provide an extension of the General Work Permit

Spaces to provide renewals of the General Work Permit for subsequent days

Space for an acceptance signature of Company’s Responsible Party or Permit Issuer to indicate satisfactory turnover of job task/site upon completion of work

Each type of permit form shall have its own individual color scheme as follows:

General Work Permit – Yellow

Confined Space Entry Form – Green

Hot Work Form – Pink

Excavation Form – Brown

Electrical Form – Blue

This may take the form of a colored border (as per example in Attachment 1) or the complete form may be printed on colored paper.

Note: Only the Permit Issuer can make changes to the information on the forms. When such changes are required, the Permit Issuer must collect the original and all copies of the work permit or form and the changes made to each one. Once the changes are made, the Permit Issuer must communicate the changes to the Permit Requester or Permit Holder, who must initial the permit/forms to denote acceptance of the changes. All work crew must be briefed on such changes before resuming work.

### Additional Work Forms

See the relevant SWP standards for other documents that may be required. For example, forms for gas detection, isolation of hazardous energy and confined space entry may be needed depending on the work that is conducted.

## Permit Changes

### Permit Extension or Renewal

The date, starting time and expiration time must always be listed in the appropriate space on the General Work Permit. An existing General Work Permit may be extended for up to a maximum of 16 total hours in the same shift, provided that the Permit Issuer is still on site. A General Work Permit may be renewed on a daily basis for up to six consecutive working days.

The Permit Issuer must perform the following steps to renew the form:

Confirm in the field that all conditions, requirements and controls listed on the permit remain in effect.

If gas testing was required by the original General Work Permit, then the responsible Qualified Gas Tester must perform new gas testing and document the results. Gas test results must be within an acceptable range or else hazards and controls must be reassessed.

Update the number of workers in attendance.

Confirm that the total allowable hours within a calendar day have not been exceeded.

Obtain the signatures of the Permit Requester and/or the Permit Holder in the extension or renewal section.

Update all copies of the General Work Permit.

Note: A permit extension or renewal may be granted only by the Permit Issuer responsible for the shift or time period in which the work is to be performed.

### Permit Revalidation

Should site conditions change or should the work stop for a period over 30 minutes with no one in attendance, the General Work Permit and any additional Work Forms must be revalidated before work can be restarted. Revalidation requires the Permit Issuer to verify that all conditions and requirements on the permit and forms remain in effect. The work may be resumed only after the Permit Issuer has given approval to restart the permitted work.

Note: Permit revalidation must be documented after the Permit Issuer has ascertained it is safe to recommence work. The revalidation of permit conditions and requirements shall be documented on the Pre-job Safety Briefing tool for that day.

### Recording Changes

Only the Permit Issuer can make changes to the information on the permits and associated forms and any changes made must be documented on all copies and communicated to the permit Requester or Permit Holder.

Note: Changes to permit form by the Permit Issuer require that all affected work crew members must be briefed on such changes before resuming work.

### Permit Cancellation

Work must be stopped and the permit canceled under any of the following conditions:

A change of the entire work crew

A change of Permit Requester or Permit Holder

A change in the scope of the work (such as the addition of work that was not originally anticipated)

The maximum hours for a calendar day are reached

A change in the job site conditions, resulting in a potential hazard, such as a leak or spill

A serious injury, incident or near miss/loss at the job site

Withdrawal of the work permit by the Permit Issuer

## Contractor Self-Permitting

Self-permitting by select contractors may be a viable option for the permitting of work if they meet all of the requirements of this standard. Each SBU/BU will make the determination if contractor self-permitting is acceptable. For the general selection requirements for contractor self-permitting, refer to the Downstream & Chemicals – Contractor HES Management Process.

## Gas Testing

Under normal circumstances, gas testing is not required for work performed under a General Work Permit. However, there may be instances when, during the hazard assessment, it is determined that gas testing will be required (for example when there is a potential for gasoline vapors, hydrogen sulfide [H2S], benzene or other gases to be present). When gas testing is required, the results must be recorded on the General Work Permit.

Refer to the Americas Products – SWP Gas Detection Standard for additional information concerning gas testing requirements.

## Preparation of Job Site and Equipment

Complete the steps needed to properly and safely prepare the job site/equipment for the start of the work as noted on the General Work Permit and related permit documentation. This step must be completed by the appropriate personnel qualified to perform such tasks.

Typical preparations may include, but are not limited to, the following:

Equipment Isolation (Refer to the Americas Products – SWP Isolation of Hazardous Energy Standard)

Depressurization

Purging, flushing, draining and venting

Barricading of the area

Gas testing if determined to be required by the risk assessment

Communication of the job task to all affected parties

## Discuss Hazards Identified, Controls and Requirements

The Permit Issuer and Permit Requester or Permit Holder must discuss at the job site the identified hazards, controls and requirements listed on the General Work Permit and, where applicable, the job safety analysis (JSA) to ensure there is mutual understanding and agreement.

## Issuing Permits

Once the Permit Issuer has entered the required information on the General Work Permit, all parties (Permit Issuer, Permit Requester or Permit Holder, and Permit Approver, if applicable) are required to sign the General Work Permit after verification of the following:

The results of the pre-job risk assessment are listed on the permit and, if determined to be high risk work, the requirements of the Americas Products – Managing SWPs Assessing Hazards and Managing High-Risk Work Procedure are followed.

All site conditions and control measures required by the General Work Permit have been implemented.

All parties are aware of the site emergency plan, should an incident occur.

All parties responsible for supervising and executing the work understand and are prepared to execute the work according to the conditions and requirements listed on the General Work Permit and related documentation.

Upon verifying the above, the Permit Issuer enters the “Valid From” or “Authorized Start” time when signing the permit.

The Permit Issuer shall retain a copy of the issued General Work Permit in accordance with Section 5.2 Retention Requirements. The original (first page) of the General Work Permit shall be given to the Permit Holder for posting at the job site.

The supervisor or appropriate person in charge shall conduct a field review of the work in progress during each shift. This is to ensure that the work plan is being followed and that conditions have not changed.

## Start Work

Work must start within an agreed time period, as designated by the Permit Issuer, when the permit is issued. If work does not start within the designated time frame, then the work permit must be revalidated. In all cases, if the work does not start within 30 minutes of the issue time listed on the work permit, the work permit must be revalidated.

## Conditions for Work Stoppage

Work must be stopped and the General Work Permit returned to the Permit Issuer for reevaluation to assess if the permit can be re-validated under the following conditions:

A serious safety concern has been raised by a worker or Company representative.

Changes in a job site condition after permit issuance is affecting the safety of the work or the workers or the job site condition has gone beyond the specified permit conditions.

Facility emergency alarms have been activated.

A minor incident or near loss at job site has occurred.

The initial time limit designated on General Work Permit has been reached.

The job site has been left unattended (for example, during a lunch break or other work stoppage), and the time elapsed has been greater than 30 minutes.

## Work Completion

When the work has been completed per the job scope, the Permit Requester or Permit Holder returns the permit and related documents to the responsible Permit Issuer. The Permit Issuer or other Person in Charge must review the job site to ensure the following conditions have been met:

The job site has been left in a safe, clean and orderly condition.

The work performed meets the scope and specifications.

When the above conditions have been met the Permit Issuer or Person in Charge shall sign and date the permit.

The job site review should be conducted by the Permit Issuer or their designee along with the Permit Requester or Holder.

# Records

## Required Records

The following records will be kept for conformance with this standard:

Copies of all work permits and associated documentation (JLAs, hazard assessments, etc.) and other work forms (see Appendix A: General Work Permit Example).

The training records of the Permit Issuer and Permit Approver or other persons, as appropriate to the work

Authorization documentation for the Permit Issuer and Permit Approver

Company BUs will maintain an up-to-date list of all contractor personnel authorized to be a Permit Issuer or Permit Approver for self-permitting (see the Downstream & Chemicals – Contractor HES Management Process for the General Qualification Guideline for Contractor Self-Permitting and the Sample Tracking Sheet for Self-Permitting.

Note: All Permit Issuers and Permit Approvers shall be so authorized in writing by the appropriate management. For contractor employees approved for self-permitting the contractor must make available to the Company copies of each Permit Issuer and Approver’s relevant training records. The Business Unit shall maintain access to an up-to-date list of those Contractors approved to self-permit and the names of their employees approved as a Permit Issuer and Approver.

Permit Issuers and/or Qualified Gas Testers shall only be authorized by management after they have successfully completed a Permit Issuer and/or Gas Tester competency evaluation. Results of such evaluations shall be valid for a 3 year period from date of completion of the competency evaluation. At the conclusion of the 3 year period the Permit Issuer/Qualified Gas Tester shall be required to retest on the competency evaluation. Self-Permitting contractors’ Permit Issuers and Qualified Gas Testers shall be authorized and approved in accordance with the requirements as agreed during the approval process for self permitting.

## Retention Requirements

All documents will be retained in accordance with the Chevron's Retention Schedule and as required by local regulations. At a minimum, records will be kept for the periods specified below:

Copies of all work permits, forms and associated documentation will be kept for one year or from audit to audit, whichever is the lesser.

Training records will be kept for personnel until five years beyond termination of employment.

Copies of letter of authorization of the Permit Issuer and Approver will be kept on file for three years, as proof of role competency.

In cases where contractor self-permitting is allowed, the Company representative or the Person in Charge will keep the list of contractors, who are authorized to self-permit, at the job site for one year.

In cases where an incident occurred at the job site while the permit was in effect, the permit form and related documents must be kept with the incident investigation documentation.

# References

Following is a complete list of the documents referenced by this standard:

Downstream & Chemicals Managing Safe Work Practices SharePoint

Americas Products Managing Safe Work Practices SharePoint

Document List

| Title | File Name |
| --- | --- |
| Americas Products – Managing SWPs Assessing Hazards and Managing High-Risk Work Procedure | AP SWP Assessing Hazards And Manage Risk Procedure.docx |
| Americas Products – SWP Gas Detection Standard | AP SWP Gas Detection Standard.docx |
| Americas Products – SWP Isolation of Hazardous Energy Standard | AP SWP Isolation Haz Energy Standard.docx |
| Downstream & Chemicals – SWP Training Requirements Tool | DS&C_SWP_TrainingRequirements_Tool.doc |
| Downstream & Chemicals – Contractor HES Management Process | DS&C_CHESM_Process.doc |
| Downstream & Chemicals – Sample General Permit Form | DS&C_SampleGenPermit_Form.doc |

# Other Guidance Documents

Document List

| Title | File/Link Name |
| --- | --- |
| American Petroleum Institute (API) Recommended Practice (RP): 505 Recommended Practice for Classification of Locations for Electrical Installations at Petroleum Facilities Classified as Class I, Zone 0, and Zone 2 500 Recommended Practice for Classification of Locations for Electrical Installations at Petroleum Facilities Classified as Class I, Division 1 and Division 2 | http://itc.chevrontexaco.com/infomAPt/library/#Standards Note: You may need a subscription to access API documentation. If so, consult a Librarian listed on the home page. |
| Americas Products – SWP Confined Space Entry Standard | AP SWP Confined Space Standard.docx |
| Americas Products – SWP Electrical Standard | AP SWP Electrical Standard.docx |
| Americas Products – SWP Hot Work Standard | AP SWP Hot Work Standard.docx |
| Americas Products – SWP Work at Height Standard | AP SWP Work Height Standard.docx |

# Revision History

Revision History

| Description | Americas Products |
| --- | --- |
| Revision Date | September 2006 |
| Next Revision Due | September 2011 |
| Control Number | APSWP208 |

Amendment Details

| Amendment Date | Detail |
| --- | --- |
| April 2009 | Americas Products Blue Text Added |
| February 2011 Terms & Definitions | Added black text to routine work definition Generally the task is performed at least once a month. There is a very low probability of change of work scope or conditions that would generate previously unidentified or unanticipated hazards |
| 4.0 Standard Instructions | Update black text of General Work Permit to The General Work Permit system serves a dual purpose: it is both an administrative control to ensure work is authorized prior to its execution and a means for identifying and communicating the precautions and restrictions necessary to perform the work safely. |
|  | Replace Global Downstream to Downstream & Chemicals, Global Marketing to Americas Products |

Appendix A: General Work Permit Example

The following is an example of the General Work Permit. The actual form consists of an original and carbon copies. In countries where English is not the predominant language, at least one of the copies shall be written in the predominant language used.

Click here to view a sample General Permit Form.